## Slide 1: Precipitation Runoff Modeling System
Model Construction

## Slide 2: File structure
bin
  contains PRMS executable
dist
  contains supporting files to run PRMS files and GUIs
projects
  contains applications of PRMS

## Slide 3: File structure
acf
  control
  input
  output
  batch files for execution of model and supporting software

## Slide 4: Files in projects/acf folder
Files in acf folder
  ACF is a batch file that executes PRMS in command line mode

## Slide 5: Files in projects/acf/control folder
acf.control is the PRMS control file that specifies the model configuration

## Slide 6: Example of control parameter
Specification of master data file (data_file)
1 – one file
4 – type ‘string’
./input/acf.data is the path to that file (can be absolute or relative)

## Slide 7: Files in projects/acf/control folder
acf.control.param is a functional PRMS parameter file that includes values specified in the parameter file and default values for any parameters used by the modules but not specified in the parameter file. (Created by executing ACF_print)

## Slide 8: Files in projects/acf/input folder
acf.data is the master data file that typically includes observations of streamflow, temperature, and precipitation

## Slide 9: Example data file

## Slide 10: Example data file

## Slide 11: Files in projects/acf/input folder
acf.params is the PRMS parameter file

## Slide 12: Example parameter file

## Slide 13: Example parameter file
  ** Parameters **
  ####
  Splits parameter file between dimensions and parameters

## Slide 14: Example parameter file
  #### - defines start of parameter field
  Parameter name (smidx_exp)
  Number of dimensions (1)
  Dimension name (nhru)
  Size of dimension (258)
  Value type (2 = float)
  Parameter values……..

## Slide 15: Example parameter file
  #### - defines start of parameter field
  Parameter name
  Number of dimensions
  Dimension name
  Size of dimension
  Value type
  Parameter values……..

## Slide 16: Example parameter file
  #### - defines start of parameter field
  Parameter name
  Number of dimensions
  Dimension name
  Size of dimension
  Value type
  Parameter values……..

## Slide 17: Example parameter file
  #### - defines start of parameter field
  Parameter name
  Number of dimensions
  Dimension name
  Size of dimension
  Value type
  Parameter values……..

## Slide 18: Example parameter file
  #### - defines start of parameter field
  Parameter name
  Number of dimensions
  Dimension name
  Size of dimension
  Value type
  Parameter values……..

## Slide 19: Example parameter file
  #### - defines start of parameter field
  Parameter name
  Number of dimensions
  Dimension name
  Size of dimension
  Value type
  Parameter values……..

## Slide 20: Example parameter file
  #### - defines start of parameter field
  Parameter name
  Number of dimensions
  Dimension name
  Size of dimension
  Value type
  Parameter values……..

## Slide 21: Files in projects/acf/input folder
Preprocessed climate-by-HRU (CBH) files for:
  Orad – solar radiation
  Prcp – precipitation
  Ptet – potential ET
  Tmax – max air temperature
  Tmin – min air temperature

## Slide 22: Example CBH file
  Comment line
  Dimension and size
  #### - start of data
  Data time series

## Slide 23: Example CBH file
  Comment line
  Dimension and size
  #### - start of data
  Data time series

## Slide 24: Example CBH file
  Comment line
  Dimension and size
  #### - start of data
  Data time series

## Slide 25: Example CBH file
  Comment line
  Dimension and size
  #### - start of data
  Data time series

## Slide 26: Geo Data Portal
https://cida.usgs.gov/gdp/