## Slide 1: Flow in Channels (SFR) and Reservoir Storage (LAK)

## Slide 2: Channel Flow (SFR)
SFR simulates streamflow using continuity
Simulating flow and depth is important for estimating SW-GW interactions
Wetting and drying of channels, impacts of capture by wells
Simulate flows where there are no measurements
Inflows and outflows from reservoirs

## Slide 3: Channel Flow (SFR)
Solves steady-flow
Kinematic-wave
Diversions, releases, floodplain

## Slide 4: Channels are Represented at Sub-grid Level
Streams divided into segments and reaches
Reach is a length of stream within one MODFLOW grid cell that has constant streambed properties.
Segments are groups of reaches that have
  Uniform overland flow, precipitation, ET
  Tributary inflow
  Point inflow or outflow at beginning
  Diversions from downstream end

## Slide 5: Stream Network and Channel Geometry
Segment 4
Model grid
Segment 1
Segment 2
Segment 3
Segment 5
Segment 6
Segment 7
Inflow
Inflow
Diversion
Point diversion
Canal delivery
for irrigation
Canal
Segment
junction

## Slide 6: Channel Flow (SFR) and Reservoir Storage (LAK)
Flow into and out of each reach calculated during every MODFLOW iteration
Multiple stream reaches simulated for a model cell
Does not simulate multiple model cells for one stream reach
1
2
3
Joining reaches
2
1
Parallel reaches
1
2
Only one cell per reach
3
GW node

## Slide 7: Stream Inflows
1
2
3
Pipeline
Start of segment 4
Inflow = pipeline + sum of tributary flows
Overland runoff
(L3/T)
L = channel length
w= width
Streambed
Reach

## Slide 8: Stream Outflows
End of segment
pipeline
Start of segment
Diversionary flow
L = channel length
w= width
Streambed
Reach

## Slide 9: Diverting Flow into a Segment
Specified diversion
  Diversion rate reduce to available flow
  Diversion rate reset to zero when available flow less than specified diversion
Specified fraction of flow in stream
Flow diverted only when available flow exceeds a specified flow rate

## Slide 10: Big Challenge: How to Create Stream Network
Creating a stream network is tricky, especially in areas with significant relief
Issues are caused by the model grid scale DEM; causes low lying cells to shift. Can’t use NHD stream network
Solution is to use combination of NHD and ARC tools to create network
Stream network and model grid DEM must be consistent

## Slide 11: NHD+ Networks not Consistent with Resampled DEM (Model Top)
Circular Flows

## Slide 12: NHD+ Networks not Consistent with Resampled DEM (Model Top)
NHD streams cut across cells above the stream canyon defined by model cells

## Slide 13: Difficulties Developing Stream Networks
Alternatively, use ArcHydro flow direction (FD) and flow accumulation (FA) tools based on model cell altitudes.
This causes problems in flat areas

## Slide 14: Hybrid NHD/ArcHydro Approach
Sequential process
Buffer model cells around NHD streams (4 cells wide)
Apply DEM (model scale) conditioning (CRT), assure continuous down-sloping paths, lower cells to deal with “holes”
Use conditioned DEM to develop streams using ArcHydro (FD+FA)
Much better!

## Slide 15: New SFR2 Features
Time series inflow to stream reach (can be any arbitrary time interval)
OPTIONS
Tabfiles 716 13219 #tabfiles, numtab, maxval
END

## Slide 16: Channel Flow (SFR)
Solves steady-flow
Kinematic-wave
Diversions, releases, floodplain

## Slide 17: Channel Flow (SFR)
Solves steady-flow
Kinematic-wave
Diversions, releases, floodplain