## Slide 1: Unsaturated Flow (UZF1) Package
1-D vertical flow beneath the soil zone.
Regional groundwater models; delay and attenuation of recharge.
Simulates ET, groundwater discharge to soil zone, and rejection of infiltration caused by shallow water table.

## Slide 2: Unsaturated Flow
Important for simulating recharge processes in regional hydrology models

## Slide 3: Why Use 1-D Kinematic-Wave Equation?
There are several reasons. A review of other approaches for simulating unsaturated flow provides impetus and justification.

## Slide 4: Difficulties with Applying Numerical Solution of Richards’ Equation for Regional Studies
Constitutive parametric models: K(Ψ) and θ(Ψ); laboratory scale.
Requires small cells (cm) to resolve infiltration and drainage.
Data limitations.

## Slide 5: Comparison between Richards-based and GSFLOW Models
GSFLOW less influenced by grid cell size
Henson, 2013
GSFLOW
Richards’ Equation
Model setup

## Slide 6: What Have We Learned from Stochastic Modeling:
“With respect to regional-scale flow processes, the solutions showed that at sufficiently large scales and in the absence of interflow, the average lateral flow component is negligible, so that the large-scale Richards’ equation becomes one-dimensional”
“The tendency of homogenizing soil water content reduces
soil water flux variability, thereby providing a justification for one-dimensional or simple bucket-type flow models to simulate regional-scale soil water flow”
Quotes from a literature review by Harter and Hopmans (2004)

## Slide 7: Derivation of Kinematic-Wave Equation
0
Chain rule
Like wave celerity in
streamflow
1D Richards’
Equation

## Slide 8: Unsaturated Flow Beneath Soil Zone— Kinematic-Wave Equation
Kinematic wave simplification of Richards’ Equation:
Equation of variation for θ:
Matrix form:
USGS
science for a changing world
Notes: Lose the hydraulic diffusivity term from Richard’s equation.

## Slide 9: Method of Characteristics Solution
Wave-velocity characteristic
Theta-loss characteristic (ET)
Wave-profile characteristic
Cramer’s rule
USGS
science for a changing world
Notes: Cramer’s Rule: if there exits a set of n linear equations, then the system has a unique solution if the determinate of the system is not equal to zero. We are looking for the discontinuity at the wave front (non-unique solution). Thus, the characteristics are found by setting the determinates to zero.

## Slide 10: Water Table is Below Land Surface: Water Table Rises
Infiltration
Increasing
New water table
level
t
t+Δt

## Slide 11: Water Table is Below Land Surface: Water Table Falls
Infiltration
Increasing
Old water table
level
t
t+Δt
Water table
falls faster
than wetting
front

## Slide 12: UZF1 Compared to Observed Field Data and Richard’s Equation
From Twarakavi et al. (2008) 7 (2) Vadose Zone Journal

## Slide 13: Comparison to Vauclin et al. (1979) Laboratory Experiment
Richards’ equation (Hydrus)
UZF1
From Twarakavi et al. (2008) 7 (2) Vadose Zone Journal
Lab experiment: Vauclin, D Khanji, G Vachaud - Water Resources Research, 1979