## Slide 1: Using the Ensemble Smoother to calibrate complex integrated hydrologic models
Ayman H. Alzraiee
California Water Science Center, U.S. Geological Survey
"Preliminary Information-Subject to Revision. Not for Citation or Distribution."

## Slide 2: Presentation Outline
Review strengths and limitations of different calibration methods.
Data assimilation (DA): justification, theoretical background, and numerical implementation.
Synthetic calibration problem to demonstrate strengths of DA.
Case Study: Calibrating Yucaipa Integrated Hydrologic Model using Ensemble Smoother.

## Slide 3: Introduction: Model Calibration
Manual Calibration – Trial and Error
Gradient-based Methods
  PEST
  UCODE
Data Assimilation-based Methods
  Ensemble Kalman Filter,
  Ensemble Smoother,
  Ensemble Kalman Smoother

## Slide 4: Gradient-based Calibration
Model
Par1
Par2
output
Gradient of the prediction error (simulated minus observed) must be computed for each parameter
The model must be run at least as many times as there are parameters.

## Slide 5: Introduction – The curse of Dimensionality
Distributed models requires the calibration of ~105 -106 of unknown parameters
GSFLOW
Input
Spatially distributed parameters
Output
Stream flow

## Slide 6: Multiple Local Minima
Gradient-based methods (Like Levenberg Marquardt method in PEST) are sensitive to the initial parameter values.
Global Minima
Local Minima

## Slide 7: The problem of Non-uniqueness
When the number of unknown parameters is larger than the number of observations, there is no unique solution for inverse problem.
Even when number of observations are more than number of unknown parameters , the inverse problem is still nonunique because of the unknown measurement errors.
Model
Model
Parameter set 1
Output
Parameter set 2

## Slide 8: Data Assimilation- Bayes’ Law
The likelihood is function of the difference between simulated and observed values.
The prior can be seen as a set of initial parameters values that reflects our prior knowledge.
For Linear models and Gaussian input parameters there is a solution for Bayes’ law that is widely known as Kalman Filter.
Prior
Likelihood

## Slide 9: Ensemble-based Methods
Geostatistical Simulation

## Slide 10: Kalman Filter
Calibrated Parameters vector
Prior Parameters vector
Prior Covariance of parameters and simulated observations
Observations vector
Covariance matrix of observation error
Innovation
Initial Values
Calibrated Values

## Slide 11: Synthetic Example – Pumping Test
Observation Wells
Pumping Well
Synthetic Model Settings
Boundary Conditions
Actual Conductivity Field
The goal is to estimate the hydraulic conductivity field at each cell.
200 random realizations for conductivity field are generated and simulated in the model.
Total number of unknown parameters is 2500.
Log(m/day)

## Slide 12: Calibration Results
Actual K Field
Ensemble Mean
Ensemble STD
(Estimation Uncertainty)
Actual K Field
Calibrated K Field
Before Calibration
After Calibration
Log(m/day)
Log(m/day)
Log(m/day)

## Slide 13: Calibration of Yucaipa Integrated Hydrologic Model
21.8 miles
12.17 miles
"Preliminary Information-Subject to Revision. Not for Citation or Distribution."

## Slide 14: Calibrated Hydraulic Properties Fields
"Preliminary Information-Subject to Revision. Not for Citation or Distribution."
Hydraulic Conductivity
Specific Yield
Specific Storage

## Slide 15: Predictive Uncertainty
"Preliminary Information-Subject to Revision. Not for Citation or Distribution."

## Slide 16: Model Fit
"Preliminary Information-Subject to Revision. Not for Citation or Distribution."

## Slide 17: Model Independent Data Assimilation Package
Supported by the USGS Water Availability and Use Science Program, a model-independent PEST++ package is being developed to implement a wide range of data assimilation methods.
For PEST users the learning curve will not be steep. Input/output handling protocols in PEST is adopted for Data Assimilation Package.
Can do both model calibration and model forecast updates.
Team members:
  Ayman Alzraiee, Jeremy White
  Michael Fienen, Randal Hunt
Project Repository
https://github.com/jtwhite79/pyemu

## Slide 18: DA Methods Support PEST-KF

## Slide 19: Summery
Data assimilation (DA) combines data and model predictions within probabilistic framework to get the best estimate of unknown input parameters and model output.
Ensemble-based DA can be used to calibrate high-dimensional parameters (~106 unknown parameters and their uncertainty).
Iterative Ensemble-based DA is an active area of research to benefit from the strengths of both Gradient-based methods and DA methods.

## Slide 20: Ensemble Kalman Filter
Ensemble Mean
Ensemble STD
Cycle 1
Cycle 2
Cycle 3
Cycle 4

## Slide 21: Advantages of Data Assimilation Methods
An ensemble of initial parameter values (Prior Ensemble) are used.
Forward runs (Sample size N) is much smaller (m~102) than the number of the unknown parameters (n~106).
Uncertainty Quantification (UQ) is built-in the data assimilation.
O(1/N)

## Slide 22: More than Parameter Calibration…
Model
Initial States
Model Predictions
Kalman Filter
Observations at time 1
Model
Model Predictions
Kalman Filter
Observations at time 2
Model
Model Predictions
Time: 1
Time: 2
Time: 3
Initial States
Initial States
Ensemble Kalman Filter
Time: 0
Time: 1
Time: 2

## Slide 23: Type of Kalman Filters
Modified from (Evenson, 2003)
Ensemble Kalman Filter
Ensemble Kalman Smoother
Ensemble Smoother

## Slide 24: Comparing calibration results with estimates from pumping tests