## Slide 1: Gsflow-Arcpy
Introduction to the GSFLOW development toolkit
Presenter: Murphy Gardner

## Slide 2: What is Gsflow-Arcpy?
Suite of Python scripts that apply Arcpy functions to input datasets and return GSFLOW input parameters
  Shapefile attribute table
  PRMS parameter files
  SFR input data for MODFLOW
Documentation
  Gardner et al 2018 – Environmental Modeling and Software Journal
  GitHub repository – includes scripts, templates, examples, and tutorial
  Jupyter workbooks

## Slide 3: Setup: Computing and Data
Computing needs
  Arc GIS 10.1 or newer
  Python 2.7
  Cascade routing tool (CRT, v 1.3.1)
  USDA Soil Data Viewer (v 6.2)
  GSFLOW (v 1.1.6 or newer)
Data needs
Digital Elevation Model (DEM)
Model boundary and model points shapefile
Vegetation and Soil data
Impervious coverage
PRISM or other gridded climate data
Observed station data

## Slide 4: Pre-process: Model Boundary and Points
Need model boundary and model points shapefiles to begin running Gsflow-Arcpy
Model boundary (study_area_path) is a polygon shapefile that delineates the active model domain
Model points (model_points_path) are read from a user created shapefile that defines model outlet, subbasin outlets, and sinks (if any)
If lakes are being modeled, a lake shapefile must also be created (lake_path)

## Slide 5: Exercise: Model boundary and model points
Model Boundary
  Use the model boundary Jupyter notebook to create watershed boundary
  This uses a single gage location and a DEM to create a boundary shapefile in ArcMap
  Subbasin points added after initial boundary is built
  Other options for creating model boundaries
    HUC basins (Geospatial Data Gateway)
    HA delineations
    Manually drawn in Arc

## Slide 6: Subbasins in PRMS
To observe flows in within a PRMS model domain, subbasins must be designated
This will provide flow volumes from all contributing HRUs at each subbasin outlet
Subbasin calibration is recommended when more than one streamgage exists in the model domain
To create subbasins, points labeled SUBBSAIN must be added to model points shapefile

## Slide 7: Pre-process: Soil Rasters for Gsflow-Arcpy

## Slide 8: PRMS soilzone parameterization
Soilzone ‘reservoirs’
  Preferential, gravity, capillary
Parameterization
  Gravity and preferential capacity
    sat_threshold
  Gravity flow
    slowcoef_lin, slowcoef_sq (to HRU)
    ssr2gw_rate (to GWR)
  Capillary storage
    soil_moist_max, soil_rechr_max
Markstrom et al 2015

## Slide 9: USDA soil survey data available online
Geospatial Data Gateway (link)
  Select by State/County
  SSURGO, gSSURGO, STATSGO
Web Soil Survey (link)
  Delineate area of interest (AOI)
  SSURGO and STATSGO

## Slide 10: USDA Soil Data Viewer add-in for Arc
Download and install Soil Data Viewer 6.2 (link)
  Follow instructions for a non-USDA CCE Platform and register as ArcMap add-in
  This may require administrator privileges

## Slide 11: Exercise - Import soil data
Unzip soil survey folder and open Microsoft Access database (.mdb) file
  Disable Macros, Enable Content if prompted
  Paste filepath to ‘tabular’ folder in the SSURGO Import pop-up
  Soil data will take a couple minutes to load
Open spatial data in ArcMap (soilmu_a_aoi.shp)
Open Soil Data Viewer
  Select the shapefile that is open in ArcMap
  Select ‘Advanced Mode’
  Select ‘Soil Physical Properties’

## Slide 12: Exercise - Import Soil Data (contnd)
PRMS requires the following soil properties
  Available Water Capacity (AWC)
  Percent sand, clay, and silt
  Saturated Hydraulic Conductivity (Ksat)
Select these (one at a time) from the list of ‘Soil Physical Properties’
  Set ‘Rating Options’ and then click ‘MAP’
  A shapefile of the soil property will appear in ArcMap
  Use the Conversion Toolbox to convert ‘Polygon to Raster’ to create .img rasters that will be read by Gsflow-Arcpy

## Slide 13: Overview of Gsflow-Arcpy components

## Slide 14: Configuration file (.ini)
Folder paths
Arcpy operational settings
Model specifications
Stream network settings
Observed climate data
Parameter and dimension CSV
Parameter file setup
Config parser Jupyter workbook

## Slide 15: Remap files
What are they and what are they used for?
  Coverage type
  Coverage density (summer/winter)
  Snow and rain interception (summer/winter)
  Root depth
  Temp adjust
Gardner and others 2018
Example: coverage type

## Slide 16: Executing the scripts
Order of operations
  Iterate for stream network
Check progress in ArcGIS
Batch file
Gardner and others 2018

## Slide 17: HRU parameter shapefile (.shp)
Shapefile that stores all parameter info as scripts are run
  Raster files
  .dbf file
Go to Jupyter workbook to begin!

## Slide 18: Stream Network and Cascade Routing
Initial stream network is based on the initial DEM_ADJ (unfilled)
Cascade routing tool (CRT) is used to fill the DEM_ADJ
  Manually filling can also take place
CRT (Henson et al 2013) defines flow paths within a grid-based watershed model for every model grid cell (HRU)
Once CRT has filled and assigned cascades per HRU, a final stream network is composed

## Slide 19: CRT fill and stream network development
Swales/sinks
Streams/lakes
Flow length/accum thresholds
CRT fill and manual adjustments
  CRT fill flag
Iterate
Go to Jupyter workbooks to build a stream network!

## Slide 20: Vegetation and Soil input
Veg
  LANDFIRE database
  EVT140 and EVC140
  Attribute data dictionary
  Check remap files
Soil
  USDA data portals
  SSURGO and/or STATSGO
  Soil Data Viewer
  Make raster images
Go to Jupyter workbooks to run the veg and soil scripts!

## Slide 21: Climate distribution
PRISM-to-station relationships
PPT/temperature zones
Station records
PRMS modules

## Slide 22: Precipitation and temperature zones
Shapefile that designates the zones and holds mean monthly observed data in the attribute table
Scripts use the shapefile to assign HRUs climate distribution values based on the zone they fall into
Go to Jupyter workbooks to run the climate scripts!

## Slide 23: Impervious cover
Recommended – NLCD Impervious coverage 2011 (link)
impervious_parameters.py
Outputs a percent impervious per HRU

## Slide 24: PRMS parameter files
Config file settings
  Array or column mode
  Single or multiple
CSV files
  Dimension and parameter settings
Go to Jupyter workbooks to run the impervious and parameter file scripts!

## Slide 25: Configuration File for Gsflow-Arcpy

## Slide 26: Folder/file paths
Specific to project names and local folders
Gsflow-Arcpy is executed from the location of the configuration file
Templates available with the Gsflow-Arcpy GitHub repository

## Slide 27: Fishnet
Framework grid
Set cell size
Fishnet and centroid path need the same root name

## Slide 28: Fishnet continued
If creating new fishnet, no reference coordinates needed
  Just need model boundary and model points shapefiles
If using an existing fishnet, this step can be skipped, or reference coordinates can be used to snap to an existing grid
Buffer cells – cells beyond model boundary

## Slide 29: DEM
Recommended - IMG file from USGS portal (link)
Set filepath (dem_orig_path)
Specify original units and resolution
Flow accumulation weighted
Initial temperature adjust is based on HRU aspect
Gardner et al 2018

## Slide 30: Stream Network
Flow accumulation and flow length thresholds
  Adjust to determine level of detail
Iterative process
  Initial network
  CRT fill
  Re-build streams after fill
  Final cascades
Gardner et al 2018

## Slide 31: CRT
Runs first without streams, to fill DEM as necessary (crt_fill_parameters.py)
  use_crt_fill_flag = True (automatically adjusts DEM_ADJ with CRT fill values)
  If set to False, DEM_ADJ values won’t change, fill amounts stored in CRT_FILL
CRT runs again with streams (stream_parameters.py)
Stream scripts must be re-run if any adjustments to DEM are made

## Slide 32: Vegetation and Soil
Set filepaths to existing vegetation type/cover data files (LANDFIRE link)
Remap files
Soil scripts read rasters created with Soil Data Viewer
  Available water capacity (AWC)
  Percent sand, silt, clay
  Saturated hydraulic conductivity (Ksat)
Option for ssr2gw_rate multiplier
  User created shapefile holding multipliers to define recharge zones, for example
  If no shapefile, default multiplier will be applied (ssr2gw_k_default)
Option for soil depth
  If not provided, root depth will be used

## Slide 33: Climate data
Single climate station
  Mean-monthly PPT data to distribute based on the station-to-PRISM relationship
  Temperature adjust based on aspect (default)
Multiple climate stations
  Designate sections of the model area to be driven by different climate stations (precip and temp zone shapefiles)
  Temperature adjustment can be based on station-to-PRISM relationship like PPT