## Slide 1
Parameter Sensitivity:
FAST and PRMS

## Slide 2: Sensitivity Analysis
Fourier Amplitude Sensitivity Test (FAST)
FAST is a variance-based global sensitivity algorithm that estimates the first-order partial variance of model output explained by each parameter
FAST has been implemented as the ‘fast’ library in the statistical software R

## Slide 3: Fourier amplitude sensitivity testing (FAST)
P1
P2
P3
Number of trials
Usim

## Slide 4: Fourier amplitude sensitivity testing (FAST)
P1
P2
P3

## Slide 5: prmsFast
Parameter sensitivity for PRMS
Written in R and Java
Sits on top of PRMS workspace
No distribution/documentation
demo

## Slide 6
Model parameters (35)
  potet_sublime
  ppt_rad_adj
  pref_flow_den
  rad_trncf
  radj_sppt
  radj_wppt
  radmax
  sat_threshold
  slowcoef_lin
  slowcoef_sq
  smidx_coef
  smidx_exp
  soil2gw_max
  soil_moist_max
  soil_rechr_max
  srain_intcp
  ssr2gw_exp
  ssr2gw_rate
  tmax_allrain
  tmax_allsnow
  tmax_index
  transp_tmax
  wrain_intcp
  adjmix_rain
  carea_max
  cecn_coef
  dday_intcp
  dday_slope
  emis_noppt
  fastcoef_lin
  fastcoef_sq
  freeh2o_cap
  gwflow_coef
  jh_coef
  jh_coef_hru
PRMS Parameter Sensitivity at CONUS Scale

## Slide 7: Dimensions of the analysis
Model parameters (35)
Output variables (8)
  Baseflow
  Actual ET
  Total contribution to streamflow
  infiltration
  Soil moisture
  Surface runoff
  Interflow
  Snowmelt

## Slide 8: Dimensions of the analysis
Model parameters (35)
Output variables (8)
Statistics for each output variable (7)
  Mean
  Coefficient of variation
  Skew
  Kurtosis
  Autoregression lag 1
  Amplitude
  Phase

## Slide 9: Dimensions of the analysis
Model parameters (35)
Output variables (8)
Statistics for each output variable (7)
Each Hydrologic Response Unit (~110,000)

## Slide 10: Dimensions of the analysis
Model parameters (35)
Output variables (8)
Statistics for each output variable (7)
Each Hydrologic Response Unit (~110,000)
10 years of daily values with 3 year warmup

## Slide 11
PRMS Parameter Sensitivity at CONUS Scale

## Slide 12
PRMS Parameter Sensitivity at CONUS Scale
Explanation
Baseflow
ET
Runoff
Infiltration
Snowmelt
Soil Moisture
Surface Runoff
Interflow

## Slide 13
Process | Performance Measure |  | 
 | Mean (Volume) | CV (Flashiness) | AR 1 (Timing)
Baseflow | jh_coef (100), soil_moist_max (91), dday_intcp (81), soil2gw_max (74), radmax (64), carea_max (37, jh_coef_hru (36) | gwflow_coef (48), soil_moist_max (40), jh_coef (28), soil2gw_max (28), smidx_coef(20), carea_max(16), tmax_allsnow(13), dday_intcp(12), smidx_exp (8) | gwflow_coef (48), soil_moist_max (44), soil2gw_max (22), carea_max (18)
Evapo-transpiration | jh_coef (100), soil_moist_max (96), dday_intcp (96), radmax (92), jh_coef_hru (62), smidx_coef (37), dday_slope (25) | radmax(100), jh_coef (100), soil_moist_max (95), dday_intcp (73), dday_slope (67), soil_rechr_max (34) | jh_coef(100), radmax(100), dday_slope(75), soil_moist_max(74), dday_intcp(67), soil_rechr_max(49)
Runoff | jh_coef(100), dday_intcp(96), soil_moist_max(96), radmax(93), jh_coef_hru(62), smidx_coef(37), dday_slope(26) | gwflow_coef(97), soil_moist_max(81), fastcoef_lin(76), pref_flow_den(71), carea_max(58), jh_coef(54), smidx_exp(49), smidx_coef(42), soil2gw_max(36), tmax_allsnow(15) | slowcoef_sq(90), soil2gw_max(90), gwflow_coef(82), carea_max(81), soil_moist_max(78), smidx_exp(72), smidx_coef(60), fastcoef_lin(36), pref_flow_den(35), jh_coef(30), slowcoef_lin(22)
Infiltration | smidx_exp(99), soil_moist_max(99), carea_max(99), smidx_coef(95), jh_coef(64), srain_intcp(50) | carea_max(80), tmax_allsnow(69), jh_coef(63), smidx_exp(62), srain_intcp(54), smidx_coef(54), tmax_allrain(48), radmax(37), freeh2o_cap(36), soil_moist_max(35), dday_intcp(31), rad_trncf(18) | carea_max(72), soil_moist_max(64), smidx_exp(61), tmax_allsnow(60), srain_intcp(60), tmax_allrain(42), jh_coef(35), smidx_coef(24), freeh2o_cap(16), dday_intcp(16)

## Slide 14
Process | Performance Measure |  | 
 | Mean (Volume) | CV (Flashiness) | AR 1 (Timing)
Snowmelt | tmax_allsnow(96), tmax_allrain(92) | tmax_allsnow(39), tmax_allrain(38), rad_trncf(9), freeh2o_cap(8), dday_intcp(7) | tmax_allsnow(34), dday_intcp(29), rad_trncf(28), radmax(24), tmax_allrain(17), jh_coef(15), freeh2o_cap(14), cecn_coef(14), emis_noppt(13), jh_coef_hru(13), potet_sublim(10)
Soil moisture | soil_moist_max(100), jh_coef(99), dday_intcp(94), radmax(82) | jh_coef(98), radmax(98), soil_moist_max(97), dday_intcp(94) | soil_moist_max(99), jh_coef(98), dday_intcp(89), radmax(35)
Surface runoff | smidx_exp(98), carea_max(98), soil_moist_max(98), smidx_coef(96), jh_coef(90), dday_intcp(33) | carea_max(93), smidx_exp(82), jh_coef(64), tmax_allsnow(55), smidx_coef(52), srain_intcp(33), soil_moist_max(23), tmax_allrain(22) | soil_moist_max(92), carea_max(83), jh_coef(65), smidx_exp(64), smidx_coef(42), tmax_allsnow(39), dday_intcp(25), srain_intcp(23), tmax_allrain(16), radmax(15)
Interflow | soil_moist_max(99), soil2gw_max(94), pref_flow_den(90), jh_coef(84), carea_max(65), smidx_exp(45), dday_intcp(31), smidx_coef(19) | fastcoef_lin(100), soil_moist_max(87), pref_flow_den(71), jh_coef(61), carea_max(49), soil2gw_max(29), smidx_exp(25), tmax_allsnow(17), dday_intcp(16) | soil_moist_max(96), fastcoef_lin(89), slowcoef_sq(83), carea_max(72), jh_coef(61), pref_flow_den(47), smidx_exp(47), ssr2gw_exp(40), soil2gw_max(26), dday_intcp(18), tmax_allsnow(16)

## Slide 15
Parameter name | Description | PRMS module
adjmix_rain | Factor to adjust rain proportion in a mixed rain/snow event | climate
carea_max | Maximum area contributing to surface runoff | surface runoff
cecn_coef | Convection con­densation energy coefficient | snow
dday_intcp | Intercept in degree-day equation | solar radiation
dday_slope | Slope in degree-day equation | solar radiation
emis_noppt | Average emissivity of air on days without precipi­tation | snow
fastcoef_lin | Linear coefficient in equation to route preferential-flow | soil-zone
fastcoef_sq | Non-linear coefficient in equation to route preferential-flow | soil-zone
freeh2o_cap | Free-water holding capacity of snowpack | snow
gwflow_coef | Linear groundwater discharge coefficient | groundwater
jh_coef | Coefficient used in Jensen-Haise potential ET computations | Potential ET
jh_coef_hru | Coefficient used in Jensen-Haise potential ET computations | Potential ET
potet_sublim | Snow sublimation fraction of potential ET | snow
ppt_rad_adj | Solar radiation adjustment threshold for precipitation days | solar radiation
pref_flow_den | Fraction of the soil zone in which preferential flow occurs | soil-zone
rad_trncf | Winter transmission coefficient for short-wave radiation | snow
radj_sppt | Solar radiation adjustment on summer precipitation days | solar radiation
radj_wppt | Solar radiation adjustment on winter precipitation days | solar radiation
radmax | Maximum solar radiation due to atmospheric effects | solar radiation
sat_threshold | Water capacity between field capacity and total saturation | soil-zone

## Slide 16
Parameter name | Description | PRMS module
slowcoef_lin | Linear coefficient for interflow routing | soil-zone
slowcoef_sq | Non-linear coefficient for interflow routing | soil-zone
smidx_coef | Non-linear contributing area coefficient | surface runoff
smidx_exp | Exponent in non-linear contributing area coefficient | surface runoff
soil2gw_max | Maximum soil water excess that is routed directly to groundwater | soil-zone
soil_moist_max | Maximum available water holding capacity of soil-zone | soil-zone
soil_rechr_max | Maximum available water holding capacity of recharge zone | soil-zone
srain_intcp | Summer rain interception storage capacity | interception
ssr2gw_exp | Non-linear coefficient in equation used to route soil-zone water to groundwater | soil-zone
ssr2gw_rate | Linear coefficient in equation used to route soil-zone water to groundwater | soil-zone
tmax_allrain | Maximum air temperature above which precipitation is rain | climate
tmax_allsnow | Maximum air temperature below which precipitation is snow | climate
tmax_index | Tempera­ture to determine precipitation adjust­ments to solar radiation | solar radiation
transp_tmax | Temperature that determines start of the transpiration period | evaporation
wrain_intcp | Winter rain interception storage capacity | interception