## Slide 1
PRMS Conceptualization of Basin Components
Modular, deterministic, distributed-parameter, physical-process, daily time-step watershed model that simulates watershed response to various combinations of climate and land use.
Precipitation Runoff Modeling System
108 Model Parameters
73 Non-calibration Parameters
  Computed directly
  Boundary conditions
  Configuration options
35 Calibration Parameters

## Slide 2
Rainfall
Snowfall
Air Temperature
Solar Radiation
Depression Storage
Snowpack Storage
Groundwater Storage
Soil Water Storage
Surface Runoff
Interflow
Base Flow
Actual ET
Recharge
Lateral Flow
Streamflow
Stream Temperature
NHM-PRMS

## Slide 3: Continuity Equation
Stream Flow
Ground Water Flow
Evapotranspiration
Trans-basin Flow
DStorage = Inputs - Output - Error
Precipitation
Ground Water
Water Bodies
Snow & Ice
Soil Moisture

## Slide 4: Units used in PRMS
Storage (volumetric) Units: Inches (depth over area)
  Example: snow pack
Flux (volumetric flow)Units: Inches (depth over area / time step)
  Example: precipitation
  This means that most continuity calculations reduce to simple additions or subtractions because “area” and “time step” cancel out and all that is left is “depth”

## Slide 5: PRMS Scale
Spatial Scale: 10s to 10,000s km2 (< 1 km2 resolution)
Temporal Scale: 1s to 100s years (daily time step)

## Slide 6: PRMS Discretization of Space
Model Domain
Stream Segments
Hydrologic Response Units
Subbasins

## Slide 7: System Concepts: Processes and Modules
A “process” represents one of the major hydrological process or administrative tasks
PRMS has 17 processes
A “module” is a piece of source code used by PRMS to simulate a process
PRMS has 39 modules
A module must be selected for each process

## Slide 8: System Concepts: Processes
Basin definition - Defines shared watershed-wide and hydrologic response unit (HRU) physical parameters and variables
Cascading flow - Determines computational order of the HRUs and groundwater reservoirs for routing flow downslope
Solar table - Compute potential solar radiation and sunlight hours for each HRU for each day of year
Time series data - Reads and stores observed data from all specified measurement stations
Temperature distribution - Distributes maximum and minimum temperatures to each HRU
Precipitation distribution - Determines the form of precipitation and distributes it from one or more stations to each HRU
Combined climate distribution - Determines the form of precipitation and distributes precipitation and temperatures to each HRU
Solar radiation distribution - Distributes solar radiation to each HRU

## Slide 9: System Concepts: Processes
Transpiration period - Determines whether the current time step is in a period of active transpiration
Potential evapotranspiration - Computes the potential evapotranspiration for each HRU for each day
Canopy interception - Computes volume of intercepted precipitation, evaporation from intercepted precipitation, and throughfall
Snow - Initiates development of a snowpack and simulates snow accumulation and depletion processes
Surface runoff - Computes surface runoff and infiltration for each HRU
Soil-zone - Computes inflows to and outflows from soil zone of each HRU
Groundwater - Sums inflow to and outflow from PRMS groundwater reservoirs
Streamflow - Computes daily streamflow as the sum of components of flow, channel routing
Summary – various output reports

## Slide 10: System Concepts: Dimensions
A value that is used to describe the array size (number of values) of a parameter or variable
Every parameter and variable has one or more dimensions associated with it
A dimension is comprised of a name and an integer value
Dimensions are read from the PRMS Parameter File

## Slide 11: System Concepts: Parameters
A static input value that does not change during the course of a PRMS simulation
“Declared” by the active modules in PRMS
Must be declared as arrays -- scalar parameters have an array size of one
Values of each parameter are read from the PRMS Parameter File before the simulation starts
Real or integer numerical type

## Slide 12: System Concepts: Variables
A value that can change each time step during the course of a PRMS simulation
“Declared” by the active modules in PRMS
Must be declared as arrays -- scalar variables have an array size of one
Input variable values of are read from the PRMS Data File as the simulation progresses
Real or integer numerical type

## Slide 13
Go through latest tables PDF

## Slide 15
Merced River Basin, California
517 km2 in area and ranges in elevation from 1200-3320m

## Slide 16
Temperature Distribution Modules
temp_1sta
Distributes air temperature to each Hydrologic Response Unit (HRU) based on a measured value
Used when temperature data from one or more measurement stations are available and the measured data can be applied to each HRU by the parameter hru_tsta.

## Slide 17: Solar Radiation Distribution Modules
ddsolrad
ccsolrad
climate_hru (CBH)
Uses measured solar radiation at a point and distribute it to
the HRUs using the calculated “clear sky” solar radiation.
If observed solar radiation is not available, estimate it.
Specified in the Control File by solrad_module

## Slide 18: Degree-Day solf Estimation

## Slide 19: Cloud Cover Solar Radiation Estimation
Estimate the amount of cloud cover on the HRU:

## Slide 20
NREL Modeled Solar Radiation
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec

## Slide 21: Solar Radiation Modules
Units
1 calorie is the amount of energy required
to raise 1 cm3 of water 1 oC

## Slide 22: Potential ET Modules
potet_jh
potet_hamon
potet_hs
potet_pt
potet_pm
potet_pm_sta
potet_pan
climate_hru
Computes potential evapotranspiration for each HRU

## Slide 23: potet_jh

## Slide 24: Computed ET (AET) as Function of PET and Soil Texture

## Slide 25: PET Maps Climatological Monthly Means (Farnsworth available on GDP)

## Slide 26: snowcomp Module
Develops a snowpack and simulates snow accumulation
and depletion processes using an energy-budget approach
for each HRU
Ffrom Koczot and others, 2005

## Slide 27: Snow Properties
Porous media
Undergoes metamorphosis
Surface albedo changes with time
Density increases with time
Has a free-water holding capacity

## Slide 28: Snowpack Description
2-layered system
Energy balance: 2 12-hour periods
Energy exchange between layers -- conduction and mass transfer
Tsurface = min (average air temperature or 0o C)
Tpack is computed
Pack water equivalent depth
3-5 cm
Tsurface
Tpack

## Slide 29: Snowpack Procedure
Precipitation added to pack
Percent snow covered area is computed
Albedo is computed
Pack depth is computed
Pack density is computed
Energy balance for night period is computed
Energy balance for day period is computed
Sublimation is computed
Snow melt is computed
For each HRU

## Slide 30
Chart: Forested Depletion Curve
| 5.0000000745060003E-2 | 0.23999999463560004 | 0.40000000596050006 | 0.52999997138980015 | 0.64999997615810035 | 0.75000000000000011 | 0.81999999284740011 | 0.87999999523160011 | 0.93000000715260001 | 0.99000000953669998 | 1
SWE | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Chart: Apline Depletion Curve
| 5.0000000745060003E-2 | 0.25 | 0.40000000596050006 | 0.47999998927120008 | 0.54000002145769999 | 0.57999998331070013 | 0.6100000143051002 | 0.63999998569490013 | 0.66000002622600018 | 0.68000000715260001 | 0.69999998807910013
 | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1

## Slide 31: Snow Surface Albedo vs Time

## Slide 32: Energy Balance Formulation
where tcalmHRU is the energy available to melt snow,
HsnmHRU is the energy gained from short wave radiation,
HlnmHRU is the energy gained from long wave radiation,
HcmHRU is the convective or sensible heat gained at the air-snow interface,
HemHRU is the latent heat (sublimation and condensation) gained at the air- snow interface,
HgmHRU is the heat gained from the ground (assumed 0.0),
HpmHRU is the heat gained from precipitation, and
HqmHRU is the heat required for internal state change
Heat available to raise the temperature of the snowpack and/or melt snow:

## Slide 33: Snow melt
snowmeltmHRU is the snowmelt on an HRU

## Slide 34
Module gwflow Baseflow Calculation
Hydrograph separation and the characteristic depletion equation (Linsley, Kohler and Paulhus):
PRMS baseflow and groundwater
storage equations:
Integration leads to storage
as a function of flow:
St
qt
T = t
St+1
Qt+1
T = t+1
gwflow_coef = -ln(Kr)